## Slide 1: Astro 331 Lesson 1
Introduction to Space
Systems Engineering
Supp Crs Mtl

## Slide 2: Lesson Objectives
Describe the desired goal of space mission design
Explain common elements shared in good definitions of systems engineering
Describe the systems engineering V-model
Explain why it is important to exercise good systems engineering early in a program

## Slide 3: Desired Goal of Space Mission Design
Want to generate a design that:
  Considers all aspects of the space mission
    Spacecraft, launch, operations, ground segment, user needs
  Meets mission requirements
  At an acceptable cost
  At an acceptable level of risk
We will delve into each of these topics in greater detail in this course

## Slide 4: Common Threads of Good SE Definitions
Top-down approach
Life-cycle orientation
Definition of system requirements
Interdisciplinary

## Slide 5: Definition of Systems Engineering
An interdisciplinary approach and means to enable the realization of successful systems. It focuses on defining customer needs and required functionality early in the development cycle, documenting requirements, then proceeding with design synthesis and system validation while considering the complete problem: operations, performance, test, manufacturing, cost & schedule, training & support, and disposal. Systems Engineering integrates all the disciplines and specialty groups into a team effort forming a structured development process that proceeds from concept to production to operation. Systems Engineering considers both the business and the technical needs of all customers with the goal of providing a quality product that meets the user needs.
International Council on Systems Engineering (INCOSE), 7670 Opportunity Road, Suite 220, San Diego, CA, USA.
interdisciplinary
defn sys rqmts
life-cycle
top-down

## Slide 6: V-model
V
Define System Requirements
Allocate System Functions to Subsystems
Detail Design of Components
Verify Components
Verification of Subsystems
Full System Operation and Verification
Integration and Verification
Decomposition and Definition
Testing
Notes: Forsberg and Mooz developed
Decomposition on the left down to an architecture, verification and testing up the right side to meet the original customer needs
At all levels the original needs and requirements are verified

## Slide 8
Need
Develop Concept
Design & Develop System
Retire System
Operate System
Deploy System
Produce System
Conceptual Design
Preliminary Design
&
Detail
Design

## Slide 10: “Best” Designs If Each Team Gets Their Way
Systems engineering is a holistic approach that considers what design choices are best for the system as a whole, not just one segment.
Notes: The best SYSTEM is the sum of the best SUBSYSTEMS
Compromises must be made in each subsystem to optimize the overall system.

## Slide 11: Life Cycle Commitment, System Specific Knowledge, & Costs

## Slide 12: Life Cycle Commitment, System Specific Knowledge, & Costs
Change is easiest early in lifecycle
Significant life cycle cost is incurred late
Commitment to an approach builds rapidly
Knowledge of the system lags behind commitment to approach
So, what do you conclude?