## Slide 1: Mission Design

## Slide 3: Requirements Vs. Constraints
Requirement
  features/capabilities/products/deliverables that expected to be delivered from the project as interim or end results
  Requirements focus on the capability of the deliverable rather than the project itself
Constraint
  factors that need to be taken into accounts when planning the project. Constraints are mostly restrictions imposed on the project. In the PMBOK® Guide, constraints include a total of 6 competing project constraints:
  Scope – what are required/expected of the project?
  Time – when will the project need to be finished?
  Cost – how much money is provided?
  Quality – what is the expectation of the outcome? high or just okay?
  Resources – who are the working team members? what equipment/materials are provided?
  Risk – what can go wrong with the project and how to deal with them?

## Slide 5
Fig 1-3 Space Mission Architecture

## Slide 6: Common System Drivers
Driver | What Limits Driver | What Driver Limits
Size | Shroud or bay size, available weight, aerodynamic drag | Payload size (frequently antenna diameter or aperture)
On-orbit Weight | Altitude, inclination, launch vehicle | Payload weight, survivability; largely determines design and manufacturing cost
Power | Size, weight (control is secondary problem) | Payload & bus design, system sensitivity, on-orbit life
Data rate | Storage, processing, antenna sizes, limits of existing systems | Information sent to user; can push demand for onboard processing
Communications | Coverage, availability of ground stations or relay satellites | Coverage, timeliness, ability to command
Pointing | Cost, mass | Resolution, geolocation, overall system accuracy
Number of Spacecraft | Cost | Coverage frequency, and overlap
Altitude | Launch vehicle, performance demands, weight | Performance, survivability, coverage (instantaneous and rate), communications
Coverage (geometry and timing) | Orbit, scheduling, payload field of view & observation time | Data frequency and continuity, maneuver requirements
Scheduling | Timeline & operations, decision making, communications | Coverage, responsiveness, mission utility
Operations | Cost, crew size, communications | Frequently principal cost driver, principal error source, pushes demand for autonomy (can also save “lost” missions)
Table 2-8 Common System Drivers

## Slide 7: Systems Engineering “V” model
When defining requirements, you are on the top left of the V, but you need to keep in mind the whole V process in order to write a good requirement.
Notes: Forsberg and Mooz developed
Decomposition on the left down to an architecture, verification and testing up the right side to meet the original customer needs
At all levels the original needs and requirements are verified

## Slide 8: Systems Engineering “V” model
verification at each level
verify complete system at the end
can’t verify complete system until the system is complete
need to verify components/subsystems along the way
allocation/closure
note what’s missing: build the system

## Slide 9: Allocation and Closure of Requirements
Allocation – assigns the function and its associated performance requirement to a lower level design element
Closure – satisfying lower-level requirements ensures system performance at the next higher level, and that we can trace all requirements back to satisfying mission needs

## Slide 10: Allocation and Closure of Requirements
Adapted from Fig 4-4 from SMAD v3
requirement allocation (big-to-little/left-to-right) and closure (little-to-big)

## Slide 11: Requirements
Requirements will usually be written as sentences or paragraphs:
Attitude control system will maintain bus pointing within 1 degree.
  Star sensors will provide accurate bus orientation knowledge with a maximum expected error of 0.2 degree.

## Slide 12: Properties of Good Requirements
Unique: no two rqmts overlap or duplicate each other
Unambiguous: no misunderstanding of exactly what is required
Testable: practical way of determining whether delivered system actually meets rqmt
Traceable: every high-level rqmt is broken down into one or more low-level testable requirements and every low-level rqmt supports a documented high-level rqmt
Consistent: doesn’t conflict with other rqmts
Specific: focuses on one thing
Essential: creates a deficiency if deleted
Complete: not missing any conditions or constraints that would distinguish an acceptable system from an unacceptable system

## Slide 13: What to Avoid in Writing Good Rqmts
Multiple Rqmts
  And
  Or
Conditional Clauses
  If
  Once
  When
  Unless
  Except
  Although
  Always
Possibilities
  Should
  Might
  Ought
  Could
  Perhaps
  Probably

## Slide 14: What to Avoid in Writing Good Rqmts (cont.)
Subjective Phrases
  User-friendly
  Easy
  Simple
  Rapid
  Efficient
  Several
  State-of-the-Art
  Improve
  Maximize
  Minimize
  Optimize
  Adequate
Subjective Phrases (cont.)
  Flexible
  Approximately
  Modern
  Versatile
  As possible
  Facilities
  Support
  High performance
  Large
  Intuitive
  Robust
  Sufficient

## Slide 16: FireSAT Requirements & Constraints
Functional Rqmts | Operational Rqmts | Constraints
Performance 30 m resolution 500 m location accuracy Coverage Daily for USA Responsiveness - Send registered data within 30 min of detecting fire to up to 50 users Secondary Mission 4 temperature levels for pest management | Duration - At leat 5 yrs Availability 98% excluding weather 3-day maximum outage Timeliness Survivability - Natural environment only Data Distribution - Up to 500 fire-monitoring office & 2000 rangers worldwide with a max of 100 simultaneous users Data Content, Form, & Format Location and extent of fire on any of 12 map bases Average temperature for each 30 square meter grid Data Storage | Cost - <$20 million/yr plus R&D costs Schedule IOC in 5 yrs FOC in 6 yrs Regulations - NASA mission (federal regs and procurement constraints apply) Political Limits - Responsive to public demand for actions Economic Return Environment Interfaces - Communication relay and interoperable through NOAA ground stations Development Constraints Launch on Shuttle or expendable No unique operations people at data distribution nodes Spacecraft Disposal
Adapted from Designing Space Mission and Systems,
Teaching Science and Technology, Inc.

## Slide 18: NASA Example
3.2 safety and mission assurance
  3.2.5 emergency equipment
    3.2.5.2 breathing mask (page 39)

## Slide 19: By next Lesson
install by next lesson:
  winget install git.git
  winget install tortoisegit