## Slide 1
Astro 331 Lesson 5
Orbit and Constellation Design
SMAD Ch 7

## Slide 2: Lesson Objectives
Describe the different orbits used throughout a spacecraft’s mission lifetime
Name commonly used mission orbits, describe their characteristics, and identify common missions that use those orbits
Describe the tradeoffs between performing a mission using a single satellite versus a constellation of satellites
Describe factors influencing the development of a spacecraft constellation
Define spacecraft orbital elements for a Walker Delta Pattern constellation and vice versa

## Slide 3: Orbit & Constellation Design Process
Insert Table 7-1

## Slide 4: Step 1: Establish Orbit Types
There are different orbits needed at different times during mission lifetime
  Parking orbit: safe & convenient temporary orbit for S/C checkout
  Transfer orbit
  Operational orbit
    earth-based: coverage of Earth’s surface or near-Earth space (ex GEO, LEO. etc)
    space-referenced: principal characteristic is a specific location in space (ex Lagrange points)
  Disposal orbit

## Slide 5: Step 2: Determine Orbit-Related Mission Reqts

## Slide 6: Step 3: Assess Standard Orbits
From Table 7-8

## Slide 7: What is a satellite constellation?

## Slide 8
Designing Space Missions and Systems, Presentation Slide S5-3: Orbit Design - 12

## Slide 9
Notes: SBIRS constellation

## Slide 10
Notes: Starlink constellation

## Slide 11
Notes: Sirius XM radio

## Slide 12: Step 4: Single Satellite vs Constellation
key trade is usually single, large S/C w/complex instruments vs constellation of smaller, simpler S/C
single S/C reduces cost by minimizing mission overhead
constellations provide
  better temporal or spatial coverage
  more robust comm links
  on-orbit spares offer higher system reliability if a S/C is lost
  more survivability
  multiple environmental conditions or geometries to carry out mission
Consider principal factors in designing a constellation (Table 7-10)

## Slide 13: Principal Factors to Consider
Insert Table 7-10

## Slide 14
Insert Table 7-10
Constellation options
  Walker Delta
  Two-Plane Polar
  Three mutually perpendicular planes
  Two perpendicular non-polar planes
  Five-plane polar “streets of coverage”

## Slide 15: Walker Delta Constellation

## Slide 16
Fig 7-14 in SMAD

## Slide 17: Step 5: Perform Mission Design Trades
Footprint area (FA or FOV area)
  area that a specific instrument or antenna can see at any instant
Instantaneous access area (IAA)
  all the area that an instrument or antenna could potentially see at any instant if it were scanned through its normal range of orientations
Area coverage rate (ACR)
  the rate at which the instrument or antenna is sensing or accessing new land
Area access rate (AAR)
  the rate at which new land is coming into the spacecraft’s access area

## Slide 18: Coverage Figures of Merit
Percent coverage
  # of times a point was covered by one or more satellites divided by the total number of simulation time steps
Maximum coverage gap
  The longest coverage gap of an individual point
Mean coverage gap
  Average length of breaks in coverage for a given point on a grid
Time average gap
  Mean gap duration averaged over time
Mean response time
  Average time from receipt of a request to observe a particular point until we can observe it

## Slide 19: Constellation Design Issues
  coverage (look at coverage (performance) vs number of S/C (cost))
  maneuvers
    avoid switching orbital planes
    limit number of planes to limit number of launches
    rephasing S/C w/in orbital plane uses very little propellant
  number of orbit planes
    #planes determines #times a given surface area can be accesses
    #S/C in a plane determine gaps in coverage
  plateaus and degradation
    each additional S/C adds performance
    graceful degradation means if one S/C fails, remaining S/C provide needed service at reduced level rather than total loss of service
    use computer modeling to assess performance
  launch vehicle selection
    try to match #orbit planes and S/C in each plane to number of S/C that can be launched on one L/V
  reasonable to begin constellation design assuming all S/C in circular orbits at same altitude and inclination

## Slide 20: Performance Plateaus
Designing Space Missions and Systems, Presentation Slide S5-3: Orbit Design - 16

## Slide 21: Step 6: Assess Orbital Transfer, Launch, and Retrieval/Disposal Options Step 7: Evaluate Constellation Growth and Satellite Replenishment
often requires numerical solns to evaluate coverage Figures of Merit
performance tends to come in plateaus (flip side is graceful degradation)
generally some performance benefit with first S/C
major performance plateau may not occur next until plane is populated or each plane has at least one S/C

## Slide 22: Step 8: Create a ΔV Budget Step 9: Iterate & Document
Account for ΔVs needed
  Think perturbations, station-keeping, momentum dumping, etc

## Slide 23: Example: Walker-Delta Constellation
Example: 15/5/2 Walker Delta Constellation
Given: COEs for 1st S/C:
  a = X km
  e = 0
  i = Y deg
  Ω = 10 deg
  u = 0 deg
Find: COEs for remaining S/C in constellation

## Slide 24: Solution
 | Orbit Plane |  |  |  | 
a (km) |  |  |  |  | 
e |  |  |  |  | 
i (deg) |  |  |  |  | 
W (deg) |  |  |  |  | 
u (deg) |  |  |  |  |