## Slide 1
Astro 331 Lesson 9
Digital Logic & Breadboarding
Supp Crs Mtl

## Slide 2: Lesson Objectives
Construct the truth table corresponding to a scenario described in words
Apply Boolean algebra to simplify a Boolean expression
Using AND, OR, and NOT gates, construct a graphical representation of a Boolean expression

## Slide 6: Boolean Algebra Laws & Theorems
X•0 = 0 | X+1 = 1 | Annulment Law
X•1 = X | X+0 = X | Identity Law
X•X = X | X+X = X | Idempotent Law
X• = 0 | X+ = 1 | Complement Law
= X |  | Double Negation Law
X•Y = Y•X | X+Y = Y+X | Commutative Law
X(YZ) = (XY)Z = (XZ)Y = XYZ | X+(Y+Z) = (X+Y)+Z = (X+Z)+Y = X+Y+Z | Associative Law
X•(Y+Z) = XY+XZ | X+YZ = (X+Y)•(X+Z) | Distributive Law
 |  | de Morgan’s Theorem
X•0 = 0 | X+1 = 1 | Annulment Law
X•1 = X | X+0 = X | Identity Law
X•X = X | X+X = X | Idempotent Law
 |  | Complement Law
 |  | Double Negation Law
X•Y = Y•X | X+Y = Y+X | Commutative Law
X(YZ) = (XY)Z = (XZ)Y = XYZ | X+(Y+Z) = (X+Y)+Z = (X+Z)+Y = X+Y+Z | Associative Law
X•(Y+Z) = XY+XZ | X+YZ = (X+Y)•(X+Z) | Distributive Law
 |  | de Morgan’s Theorem

## Slide 8: Breadboard Layout
OR
NOT
AND
AND

## Slide 9: Example
Create a truth table that represents all possible scenarios for wanting to buy a coke from a vending machine.
  First item: vending machine must have a coke in stock
  Second item: I must have exact change
  Third item: I must have a dollar bill
Then, present the Boolean algebra statement that represents all scenarios that result in success and draw a logical schematic that illustrates that statement.

## Slide 10: Solution (1/3)
Inputs |  |  | Output
In Stock A | Exact Change B | Dollar Bill C | Coca Cola Y = A(B+C)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Success:

## Slide 11: Solution (2/3)
) Associative/Distributive Laws
) Idempotent Law
)) Associative Law
)) Distributive Law
)) Complement Law
) Identity Law
Answer makes sense: I can get a coca cola if it is in stock AND I have either exact change OR a dollar bill.

## Slide 12: Solution (3/3)
Schematic from simplified Boolean expression:
Requires:
1 AND Gate
1 OR Gate
0 NOT Gates
A
B
C
(B+C)
Y = A(B+C)