## Slide 1: Digital Logic/Breadboard
OCP

## Slide 2: Boolean Logic
3 Primary Operators
  AND, OR, NOT
# of outcomes depends on number of inputs
Two states for a Binary Signal | 
TRUE | FALSE
On | Off
1 | 0
5 volts (or less in modern circuits) | 0 volts

## Slide 3: Digital Logic Gates
The “AND” Gate
A | B | Output (Q)
0
1
0
0
0
0
0
0
1
1
1
1
If both inputs are true, then output true
Math Symbol:
Boolean Equation:
Wiring Symbol:
* x ∙ ()
A ∙ B = Q
A
B
Q

## Slide 4: Digital Logic Gates
The “OR” Gate
If either input is true, then output true
A | B | Output (Q)
0
1
1
1
0
0
0
0
1
1
1
1
Math Symbol:
Boolean Equation:
Wiring Symbol:
+
A + B = Q
A
B
Q

## Slide 5: Digital Logic Gates
A | Output (Q)
The “NOT” Gate
0
1
0
1
Output is opposite of the input
Math Symbol:
Boolean Equation:
Wiring Symbol:
A’
A
A’ or
A’ = Q

## Slide 6: Boolean Algebra
Identity Element
a+0=a
a+1=1
a*0=0
a*1=a
Involution
(a')'=a
Complementation
a+a'=1
a*a'=0
Idempotency
a+a=a
a*a=a
Associative (grouping doesn't matter)
a+(b+c)=(a+b)+c
a*(b*c)=(a*b)*c
Commutative (order doesn't matter)
a+b=b+a
a*b=b*a
Distributive for BOOLEAN ALGEBRA
a+(b*c)=(a+b)*(a+c)
a*(b+c)=(a*b)+(a*c)
Absorption
a+a*b=a
Adjacency
a*b+a*b'=a

## Slide 7: Combinations and Simplifications (using Boolean Algebra)
A + A’ = 1
1 + 0 =
0 + 1 =
1
1
A · 1 = A
1 · 1 =
0 · 1 =
1
0
A + 1 = 1
1 + 1 =
0 + 1 =
1
1
Notes: These are the three most useful boolean identities, for this class. There are a number more discussed in your reading, that you are welcome to use.

## Slide 8: Logic Circuit Example Problem
At a particular zoo, some of the Lions are grouped together and given a large, open common area to use.
All of the animals have separate cages, but can access the common area at will, through a door in their cages.
The zookeepers must sometimes go into the common area to do routine tasks such as cleaning, replacing plants, and other maintenance.
Three of the Lions (Showoff, Grumpy, and Lady) are dangerous to zookeepers under certain conditions.
  See next slide for details
Your task is to design a silent (i.e., LIGHT) alarm that will warn the zookeepers if it is dangerous to be in the common area.

## Slide 9
Step 1: Determine Inputs and Outputs
S
G
L
  Showoff is not dangerous by himself, but if any of the others are present they will hunt anyone in the common area.
  Grumpy gets agitated when his mate (Lady) is not present, and will hunt the zookeeper under those conditions, but .
  Lady will hunt with Showoff, but will calm Grumpy and the pair (Lady and Grumpy) are not dangerous when alone together.
Common Area Safe to enter?

## Slide 10
How many inputs?
What are the inputs?
How many outputs?
What are the outputs?
Step 1: Determine Inputs and Outputs
3
1. Showoff is present
2. Grumpy is present
3. Lady is present
1
Silent Alarm

## Slide 11
Step 2: Derive the Truth Table
S | G | L | SILENT ALARM
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
0
0
1
1
0
0
1
1
Showoff is not dangerous by himself, but if any of the others are present they will hunt anyone in the common area.
Grumpy gets agitated when his mate (Lady) is not present, and will hunt the zookeeper under those conditions, but .
Lady will hunt with Showoff, but will calm Grumpy, and the pair (Lady and Grumpy) are not dangerous when alone together.

## Slide 12: Step 3: Write the Logic Equation from Truth Table - Use only those inputs where the alarm goes off… where the answer is SILENT ALARM = 1 (ON)
S | G | L | SILENT ALARM
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 13: Step 3: Write the Logic Equation from Truth Table - use only those inputs where the alarm goes off… where the answer is SILENT ALARM = 1 (ON)
S’·G ·L’
S·G’ ·L
S·G ·L’
S·G ·L
S | G | L | SILENT ALARM
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 14
S is not there and G is there and L is not there  S’·G ·L’
or
S is there and G is not there and L is there  S·G’ ·L
or
S is there and G is there and L is not there  S·G ·L’
or
S is there and G is there and L is there  S·G·L
… as a complete equation this is …
ALARM = S’ ·G ·L’ + S ·G’ ·L + S·G·L’ + S·G·L
In words, the Truth Table says the Alarm will go off if:

## Slide 15
ALARM = G·L’ + S·L
In Words: The alarm will sound if Grumpy is present AND NOT Lady, OR if Showoff AND Lady are present together.
Step 4: Simplify the Boolean Logic Equation ALARM = S’ ·G ·L’ + S ·G’ ·L + S·G·L’ + S·G·L Rearrange to put terms with common variables together ALARM = S’ ·G ·L’ + S·G·L’ + S ·G’ ·L + S·G·L Pull out like terms ALARM = G ·L’(S’+S) + S ·L(G’+G) From Boolean Identities , recall that a + a’ = 1 (that is, a or a’ = 1) so reduce to
ALARM = G ·L’(1) + S ·L(1) Again, recall from Boolean Identities that a*1 = a (that is, a and 1 = a) so reduce to

## Slide 16: Step 5: Draw simplified circuit
GL’+SL
L
G
S
Alarm
L’
GL’
SL
ALARM = G·L’ + S·L

## Slide 17
What does this really look like?
Need:
  NOT (1)
  AND (2)
  OR (1)
Step 6: Implement in Hardware

## Slide 18
NOT
AND
OR
L
G
S
Alarm

## Slide 19
Chip 04
NOT Gate (‘)
Chip 08
AND gate (x)
Chip 32
OR gate (+)

## Slide 20: We should adjust our diagram to show pin numbers
NOT
AND
OR
L
G
S
Alarm
1
2
1
2
4
5
1
2
3
3
6

## Slide 21
L
L’
S
G
GL’ + SL
ALARM

## Slide 22: We should adjust our diagram to show pin numbers
L
L’
S
G
GL’ + SL
ALARM
1
2
3
4
5
6
1
2
3
4
5
6
1
2
3
4
5
6

## Slide 23: Troubleshooting
When you get stuck, try on your own (in your group) to figure out what’s wrong.
In the context of this course, it is always safe to connect a multimeter in volt mode.
The simplest thing to do is check voltages down the chain of your circuit to see whether it matches your expectation.
  power supply providing 5V/ground?
  breadboard rails providing 5V/ground?
  circuit inputs?
  intermediate connections?
  circuit output?

## Slide 24: Breadboard

## Slide 25: Gates