## Slide 1: Lesson 6
Space Environment

## Slide 2: Why Worry about the Space Environment?
Approximately 25% of all spacecraft anomalies are related to the space environment.
Famous examples include:
  2010: Control of Galaxy 15 lost due to electrostatic discharge cause by solar flare. Satellite drifted through crowed GEO belt in full send and receive mode
  2009: Iridium satellite destroyed when it collided with the dead Cosmos 2251 satellite (space debris)
  2000: Boeing 702 satellite (Anik F-1): degraded solar array performance due to outgassing induced fogging
  2000: Stardust comet flyby spacecraft blinded and sent into safe mode by a solar flare
  1994: Telsat Canada’s Anik E-1 and E-2 suddenly began to spin out of control due to spacecraft charging
  1990: High energy charged particles caused bit flips in HST fine guidance system electronics (FGS) passing through the South Atlantic Anomaly (SAA) causing guide star acquisition failures. Subsequently, FGS use was suspended in the SAA.
  1979: Increased solar activity heated the outer layers of the Earth's atmosphere and thereby increased drag on Skylab, leading to an early reentry.
Warning- Traffic Hazard!. Iridium Collision with Cosmos 2251
Beware - Outgassing. Anik F-1 degraded performance due to outgassing
Caution - Solar Flare. Stardust spacecraft was blinded by a solar flare
Adapted from Designing Space Missions and Systems,
Teaching Science and Technology, Inc

## Slide 3: Terms
Hardening
Design choice when building a space system to mitigate the negative impacts of the space environment or potential hostile action (eg: shielding, filtering, etc)
Survivability
Ability of space system to perform its mission after being exposed to a stressing environment or hostile action

## Slide 4: Space Environmental Influences
Microgravity
Vacuum
Atmosphere
Plasma
Radiation
Micrometeroids & Orbital Debris

## Slide 5: Microgravity

## Slide 6: Microgravity
Source:
  Spacecraft is in free fall, where it is continuously falling through space where the forward velocity of the spacecraft is enough to match the velocity that would pull the spacecraft back toward the Earth’s surface
Effects on spacecraft:
  Fluid containment is a challenge
  All articles must be secured
  Allows uniform mixing of solutions
  Allows opportunity for new manufacturing techniques
Strategies to mitigate effects:
  Pressurize liquids/gases in containers
  Secure all components

## Slide 7: Vacuum

## Slide 8: Vacuum
Source:
  No air in space
Effects on spacecraft:
  UV radiation causes coating and materials to degrade
  Outgassing: spurious release of molecules that contaminate surfaces
  Cold welding: unintended material bonding when the atmosphere between surfaces is absent
Strategies to mitigate effects:
  Use coatings that protect against UV radiation and do not outgas
  Vent propellant/gas away from sensitive surfaces
  Don’t put metal objects that are vulnerable to cold welding near each other
  Vacuum bake-out on ground

## Slide 9: Atmosphere

## Slide 10: Atmosphere (1/3)
Source:
  Particles in air around Earth
Effects on spacecraft:
  Atomic oxygen: predominant atmospheric constituent from 200-600 km, forms when UV radiation dissociates molecular oxygen (Fig 8-5)
  Atmospheric Drag
Strategies to mitigate effects:
  Choose materials resistant to atomic oxygen or use protective coatings
  Shield sensitive surfaces, design S/C with low coefficient of drag
  Operate at higher altitudes if possible

## Slide 11: Atmosphere (2/3)
Atomic Oxygen
  Reacts with thin organic films, advanced composites and metallized surfaces
  Degrades sensor performance
  Weakens spacecraft structures
  Density of atomic oxygen varies with the solar cycle
    Solar cycle is periodic change in the amount of material and radiation emitted by the Sun and observed on Earth
    Average of 11-year cycle; shortest was 9 yrs, longest 14 yrs
    Solar maximum has many solar events; solar minima has almost no solar events
    Solar flux varies substantially on a day-to-day basis and is difficult to predict at any given future time; however, average over an extended period is well known
    Fig 8-1 depicts the F10.7 index, which is the mean daily flux at 10.7 cm wavelength in units of 10-22 W/m2·Hz

## Slide 12: Atomic Oxygen

## Slide 13: Atmosphere (3/3)
Atmospheric Drag
  Depends on a variety of factors, including S/C ballistic co-efficient, speed and atmospheric density
  Atmospheric density is highly dependent on solar cycle
  Thermosphere: (120-600 km altitude), region where absorption of extreme UV radiation results in rapid increase in temperature with altitude
    Heating due to EUV radiation and solar cycle variation impacts atmospheric density and has the greatest effect on satellite lifetimes

## Slide 14: Solar Cycle

## Slide 15: Impact of Solar Cycle on Atmospheric Density

## Slide 16: Impact of Solar Cycle/Ballistic Co-efficient on Satellite Lifetimes

## Slide 17: Plasma

## Slide 18: Plasma (1/2)
Plasma consists of neutral particles, positive ions, and electrons.
  The most abundant matter in the universe (99% of universe mass)
Source:
  Formed from interactions between solar wind and Earth’s magnetic field, stretches into long structure known as the magnetotail
  Can also come from solar flares or galactic cosmic rays (GCRs)

## Slide 19: Plasma (2/2)
Effects on spacecraft:
  Energized plasma (particles with energy from 5 keV to 50 keV) can extend into geosynchronous orbits, charging the surface of any spacecraft to high negative voltages
  Electrostatic arcs can cause electromagnetic interference (EMI) on spacecraft, causing erratic behavior
  Surface Charging that impacts spacecraft operations occurs in orbits where electrons with energies of 10-20 keV dominate the electron current
    At low altitudes, this occurs only at high latitudes (where auroral electrons collide w/ vehicle)
    At higher altitudes, surface charging occurs during magnetospheric substorms
  Ion drag that adds to orbital decay
  Ion sputtering that increases surface erosion
Strategies to mitigate impacts:
  Prevent differential charging of surfaces by ensuring entire surface is made of a uniform conductivity
  Balance currents using special surface coatings
  Grounding, selecting insulating surface materials, shielding, filtering, proper handling procedures

## Slide 20: Earth’s Magnetosphere

## Slide 21: Radiation

## Slide 22: Radiation
Sources:
  Galactic Cosmic Rays (GCRs) are high-energy particles from outside the solar system
  Solar Particle Events (SPEs) when large amounts of particles are spewed from the Sun
  Van Allen radiation belts
Effects on spacecraft:
  Can cause Single Event Phenomenon (SEP), which can have three effects:
    Bitflip/Single Event Upset (SEU) – changes one bit
    Single Event Latch-up (SEL) – part hangs up, draws excessive current, will not operate until power cycled
    Single-Event Burnout (SEB) – causes device to fail permanently
  Can generate background noise and produce spurious signals in various sensors
Strategies to mitigate impacts:
  Shielding sensitive electronics
  Design and parts selection (use radiation tolerant parts)
  Redundancy
  EDAC (error detection and correction – more to come on this in the TT&C lesson)

## Slide 23: Van Allen Radiation Belts
Regions of high-energy particles, mainly protons and electrons, held captive by Earth’s magnetic influence
Permanent hazard to orbit spacecraft, with particles distributed non-uniformly with Earth’s magnetosphere
South Atlantic Anomaly is a volume of space centered on South America’s east coast, where Earth’s inner Van Allen belt comes closest to the surface due to a weakness in Earth’s magnetic field
  An increased flux of particles exists within this space and exposes spacecraft to higher than usual radiation levels

## Slide 24: Van Allen Radiation Belts
Designing Space Missions and Systems, Fig 8.5

## Slide 25: South Atlantic Anomaly

## Slide 26: COTS vs Rad Hard Parts

## Slide 27: Micrometeroids & Orbital Debris

## Slide 28: Micrometeoroids and Orbital Debris (MMOD)
Source:
  Defunct spacecraft, rocket bodies and spacecraft debris are still in orbit and are not controlled
Effects on spacecraft:
  Kinetic damage from collision
Strategies to mitigate impacts:
  Choose orbits with minimal debris (if possible)
  Have additional propellant on-board for collision avoidance maneuvers
  Plan to dispose of spacecraft at end of mission life

## Slide 29: Orbital Debris
Source: NASA Orbital Debris Program Office

## Slide 30: Debris Mitigation

## Slide 31: Space Environment (Key Takeaways)