## Slide 1
Astro 331 Lesson 19
Electrical Power Subsystem (EPS)
SMAD Ch 5.1, 11.4, Supp Crs Mtl

## Slide 2: Lesson Objectives
Explain spacecraft power functions
List and describe typical system-level parameters that impact power subsystem design
List and describe common spacecraft power sources
Explain what a I-V plot of a planar array describes, and how temperature changes the I-V curve
Calculate solar array area to support a space mission
Understand how depth of discharge of a battery impacts the cycle life of a secondary battery
Calculate battery capacity to support a space mission
Calculate the beta angle for an orbit and understand its importance when calculating eclipse duration

## Slide 6: Spacecraft Power Sources (1/2)
Photovoltaic
    converts incident solar radiation to electrical energy
    15%-30% efficient (varies based on solar cell technology)
Static power
    converts heat directly to electrical energy
    thermoelectric energy conversion approach
        use thermocouple: uses temperature gradient between p-n junction to create electricity
        5% - 8% efficient
    thermionic energy conversion approach
        hot electrode sends ions to cooler electrode in sealed enclosure w/ ionized gas
        often use reactor heat source b/c high temp required
        10%-20% efficient
    heat sources: plutonium-238, uranium-235 nuclear reactor

## Slide 7: Spacecraft Power Sources (2/2)
Dynamic power
    Uses a heat source and a heat exchanger to drive an engine in a thermodynamic approach
    heat sources: concentrated solar radiation, radioisotopes or a controlled nuclear-fission reaction
    thermodynamic cycles:
        Stirling-cycle (25%-30%)
        Rankine-cycle (15%-20%)
        Brayton (20%-35%)
Fuel cells
    convert chemical energy of an oxidation reaction to electrical energy
    most popular version for space applications is hydrogen-oxygen (“alkaline”) resulting in electricity and water
    reactants are consumables and therefore life-limiting
    common on crewed missions b/c of useful by-product: water
    50%-80% efficient

## Slide 8: Spacecraft Power Sources
Griffin and French, Space Vehicle Design, Figure 10.2

## Slide 9: I-V Plot

## Slide 10: I-V Plots
Three significant points for solar array design:
  Short-circuit current, where voltage = 0
  Peak-power point, where voltage times current is maximized
  Open-circuit voltage, where current = 0

## Slide 11
Earth’s Angular Radius

## Slide 12: Earth’s Angular Radius
Where
= radius of the Earth (km)
h = altitude of orbit (km)

## Slide 15: Beta Angle
Where
= Ecliptic True Solar Longitude (deg), changes with date (deg); Note: * when the Sun is at the Vernal Equinox
= Right Ascension of the Ascending node of orbit (deg)
= Inclination of orbit (deg)
= Obliquity of the Ecliptic (deg);
*Note that the beta angle is limited by
- Beta angles are positive where the Sun is north of the orbit
- Beta angles are negative when the Sun is south of the orbit

## Slide 16: Calculating Solar Array Size
Want to determine how large the solar array must be in order to give us the desired power
Overall strategy:
  is end of life power produced by S/A
  is power required from S/A to meet S/C needs

## Slide 17: Power Required
Where
Pe = power required by S/C during time in eclipse (W)
Te = time in eclipse (s)
ηe = efficiency of transferring power from S/As to batteries and then to loads during eclipse (unitless) (typically 0.6-0.65)
Pd = power required by S/C during time in daylight (W)
Td = time in daylight (s)
ηs = efficiency of transferring power from S/As directly to loads during sunlit portion of orbit (unitless) (typically 0.8-0.85)

## Slide 18: Calculating Time in Daylight
Recall that we can only collect solar energy when S/C is in sun
Where
= time in daylight (seconds)
P = period of orbit (seconds)
  = time in eclipse (seconds)
= twice the rotation angle corresponding to the eclipse duration (deg)

## Slide 19
Where
= Earth’s angular radius (deg)
= beta angle, which is the angle between the solar vector and its projection into the orbit plane (deg)

## Slide 20: Power at Beginning of Life
Where
= amount of power S/A is able to produce at the beginning of its life (W)
S = solar flux (W/m2)
η = solar cell technology efficiency (unitless)
= inherent degradation (unitless) (average ~0.77, ranges from 0.49 – 0.88)
θ = sunlight incidence angle on S/As (deg)
A = S/A surface area (m2)

## Slide 21
θ = sunlight incidence angle on S/As (deg)
*Note: even sun tracking S/A may not achieve θ = 0 deg under all orbit conditions
(“sun tracking” ≠ 0 deg incidence angle)

## Slide 22: Solar Flux
 | Solar Flux (Watt/m2)
Mercury | 9127
Venus | 2615
Earth | 1367
Mars | 589
Jupiter | 50
Saturn | 15
Uranus | 4
Neptune | 2
Pluto | 1

## Slide 23: Solar Flux
Solar flux varies with the square of the distance from the Sun (like all electromagnetic waves)
Where
= Solar flux (W/m2)
= luminosity of the Sun (
dist from Sun = distance from Sun (m)

## Slide 24: Power at End of Life
Where
= amount of power S/A is able to produce at the end of its life (W)
degradation/year = percent degradation per year (in decimal form, unitless)
~3.75%/yr for Si
~2.75%/yr for GaAs
satellite life = mission lifetime (yrs)

## Slide 25: Solar Array Types
Selection of type of solar cells is based on efficiency, degradation, cost, etc.

## Slide 26: Solar Array Degradation
Solar cells degrade over time due to a variety of factors, which sum to give inherent degradation

## Slide 27: Solar Array Approach
Estimate S/A area (A) to produce necessary power (Preq) based on PEOL
Recall overall strategy:
solve for A

## Slide 28: Energy Storage
necessary to store energy for peak power demands and eclipses
batteries a convenient way to do those (other options: fly wheels, fuel cells)

## Slide 29: Primary Batteries
Non-rechargeable
High energy densities

## Slide 30: Secondary Batteries
Rechargable, but cycle-life limited
Lower energy densities
Space-qualified

## Slide 31: Depth of Discharge
Designing Space Missions and Systems, Figure 11.24

## Slide 32: Calculate Battery Size
Where
= battery capacity (W·hr)
= power required by S/C during eclipse (W)
= time in eclipse (hrs) (not seconds!)
= depth of discharge (%)
= number of batteries
= battery efficiency (converting chemical energy back to electrical); typical value is = 0.9

## Slide 34: Example
Given: A synthetic aperture radar (SAR) satellite on a 5-year mission requires 900W of power at all times. Its COEs are:
a = 7578 km
e = 0
i = 45°
Ω = 30°
ω = 270°
Uses silicon solar cells with 18% efficiency
Efficiency of power transfer in sunlight: 0.85
Efficiency of power transfer in eclipse: 0.65
Inherent degradation of solar cells: 0.75
Worst-case sun incidence angle: 30°
You may assume worst-case beta angle
Find: How big must the solar arrays be in order to provide the required power with a margin factor of 120%? Assume worst-case time in eclipse for your calculations.

## Slide 35: Solution (1/3)
Recall the strategy:
Problem states that we need to apply 120% margin:
Substitute in and then use algebra to solve for A.

## Slide 36: Solution (2/3)
Need to solve for time in eclipse first.
Where
Where
To have worst-case time in eclipse, we need the maximum value for . To get the maximum value for , the value inside the cosine term must be maximized. However, since is fixed with altitude, to maximize , the beta angle must be zero.
If we set = 0°, we get:

## Slide 37: Solution (3/3)
Next, we can get time in daylight.
Since we are talking about an orbit around the Earth, we can use (given on your eqn sheet).
Degradation of silicon cells is 3.75% per year.
Now, substitute everything in and solve for area.