## Slide 1
Astro 331 Lesson 15
Communications Architecture
SMAD Ch 13.1, 13.3, 13.5.3, Supp Crs Mtl

## Slide 2: Lesson Objectives
Label the pieces in a satellite communications architecture (i.e. uplink, downlink, forward link, return link, crosslink, relay satellite)
Describe the difference between point-to-point and broadcast communications architectures
List and describe the criteria for selecting a communications architecture
Perform link analysis calculations in real numbers and decibels
Understand the sources of noise in a link budget
Understand what jamming is and some techniques to reduce its effects

## Slide 3
Fig 13-1 The Communications Architecture Consists of Satellites and Ground Stations Interconnected with Communications Links

## Slide 4
Fig 13-2 Typical Communications Architectures Used to Satisfy Different Mission Requirements

## Slide 6
Figure from https://www.worldteleport.org/news/442460/DoDs-Automated-Satellite-Roaming-How-the-technology-protects-against-denial-of-satellite-services.htm

## Slide 7: Link Budgets & Noise Sources
= ratio of received energy-per-bit to noise-density
P = transmitted power (W)
= transmitter to antenna line loss (unitless < 1)
Gt = transmitter antenna gain (unitless)
Ls = free space path loss (unitless < 1)
Lm = miscellaneous loss [Note: SMAD uses La for transmission path loss, but we will discuss more noise sources that make up this miscellaneous term – see Supp Crs Mtl] (unitless < 1)
Gr = receiver antenna gain (unitless)
k = Boltzmann’s constant (1.38 * 10-23 J/K)
Ts = temperature of receiver system (K)
R = data rate (bits per second)

## Slide 8: Link Budget in Decibels
In decibels:
= ratio of received energy-per-bit to noise-density (db)
P = transmitted power (dBW)
= transmitter to antenna line loss (dB < 0)
Gt = transmitter antenna gain (dB)
Ls = free space path loss (dB < 0)
Lm = miscellaneous loss [Note: SMAD uses La for transmission path loss, but we will discuss more noise sources that make up this miscellaneous term – see Supp Crs Mtl] (dB < 0)
Gr = receiver antenna gain (dB)
Ts = temperature of receiver system (K)
R = data rate (bits per second)

## Slide 9: Antenna Gain
G = antenna gain (unitless)
Dr = receiver antenna diameter (m)
= signal wavelength (m)
= antenna efficiency (typically 0.55-0.7 for parabolic dishes)

## Slide 10: Antenna Beamwidth
For a parabolic antenna, an estimate of the half power beamwidth is:
fGHz = frequency (GHz)
D = antenna diameter (m)
Note: as D↑: G↑ but 3db↓ (transmit power doesn’t change but is concentrated in smaller area)

## Slide 11: Effective Isotropic Radiated Power (EIRP)
(unitless)
EIRP = power isotropic antenna (G=1) would have to broadcast at to get the same signal strength that is present at the peak power point on the beamwidth of the antenna with gain
  Isotropic: having the same property in all directions (ie, transmitting in all directions with same power level)
Can achieve same EIRP by decreasing power but increasing gain (smaller beamwidth also results)

## Slide 12: Free Space Path Loss, Ls
(unitless)
= signal wavelength (m)
S = signal path distance (range between transmitter and receiver) (careful of units: m vs km)

## Slide 13: Miscellaneous Losses, Lm
Pointing loss due to transmitter (dB)
Pointing loss due to receiver (dB)
Polarization losses (dB)
Atmospheric losses (dB)
Rain losses (dB)
[Details in supplemental reading]

## Slide 14: Antenna Pointing Loss, Lpoint
e = off-axis pointing error (angle in degrees)

## Slide 15: Polarization Mismatch Loss, Lpolar
(unitless)
Lpolar = linear polarization loss (for vertical or horizontal polarized signals but not left or right handed circular polarized)
= misalignment angle btw transmit and receive antennas

## Slide 17: Atmospheric Loss
water vapor (~22 GHz) and
oxygen (~60 and ~119 GHz)
= elevation angle (deg or rad)
zenith attenuation is looked up on a chart (dB)
[like Fig 13-10]
*Note: Atmospheric loss must be used as a NEGATIVE dB because it’s a loss!

## Slide 18: One-way Zenith Attenuation

## Slide 19: Rain Loss, Lrain
Frequency | Lr
f < 6 GHz | 0 dB
6 GHz < f < 18 GHz | -7 dB
f > 18 GHz | loss of link

## Slide 20: Rain Attenuation (Washington, DC)
Similar to Fig 13-11 for Rain Attenuation

## Slide 21: Example
For the following parameters, you may assume a circular orbit and parabolic dishes for both transmit and receive.
Find: Eb/N0

## Slide 22: Answer
Answer
Eb/N0 = 2,258,882.795 (unitless)
Eb/N0 (dB) = 63.539 dB
This is very large. We typically would like to see Eb/N0 > 9 dB, so this link has tons of margin. However, 4-meter and 6-meter dishes are much larger than what we typically have on spacecraft. The pointing error values here are also quite small (which means very precise pointing).