## Slide 1
Astro 331
Thermal Control Subsystem (TCS)
SMAD Ch 11.5

## Slide 2: Lesson Objectives
Explain spacecraft thermal control functions
List and describe the sources of heat on a spacecraft and when they apply
Describe reflectivity, absorptivity, transmissivity, and emissivity
List and describe methods of spacecraft thermal control and distinguish between passive and active approaches
Identify conditions which lead to spacecraft worst case hot and worst case cold equilibrium temperatures
Calculate equilibrium temperatures for spacecraft

## Slide 3: TCS Functions
Maintain all S/C components w/i their required temperature limits during all mission phases
  Cold temp that a component must not go below
  Hot temp that a component must not go above
Relevant temps:
  Operating limits: component must remain within these temperature ranges while operating
    if operational limits are exceeded, equipment could display out-of-tolerance behavior
  Survival limits: component must remain within these temperature ranges at all times, even when not powered
    if survival limits are exceeded, component could suffer permanent damage and potentially not turn on

## Slide 4
Adapted from Designing Space Missions and Systems, Table 11-42

## Slide 5: Thermal Radiation Environment

## Slide 6: Sources of Heat on a S/C
Direct Solar:
  Varies with 1/r2 with distance from Sun
  base value (1367 W/m2) is same as solar flux for solar array calcs
Albedo: solar energy reflected off surface of Earth
  depends on reflective properties of particular part of Earth
  because there tend to be more snow/ice near poles, they tend to have a higher reflectivity
Earth IR: thermal energy originating from Earth
  Tends to emit more radiation closer to equator and less at poles
Internal Heat generation onboard S/C
  Upper limit is total S/C power excluding that which is transmitted (ie communications)

## Slide 8: Methods of Heat Transfer
Three ways to move heat
  Conduction*: thermal power transfer through matter in absence of fluid motion
  Convection*: thermal power transfer btw flowing fluid and a solid surface
  Radiation: thermal power transfer via electromagnetic waves
  *Can move heat around S/C, but not outside of S/C

## Slide 9: Heat Emission
All bodies above absolute zero Kelvin emit according to Stefan-Boltzmann eqn
Where
  Q is energy transfer rate (W=J/s)
  ε is emissivity (unitless)
  σ is Stefan-Boltzmann constant
  A is surface area radiating (m2)
  T is temperature (K)

## Slide 10: Thermal Equilibrium
is reflectivity
is absorptivity
is transmissivity

## Slide 11: Emissivity
is emissivity (% energy emitted compared to perfect black body)
  black body is a perfect emitter:
  black body is a perfect absorber:
and vary with wavelength, but :
  most energy absorbed occurs in the solar band
  most energy emitted in infrared band
  selective surfaces: avg absorptivity in the solar band, , is much different than avg emissivity in IR band,
  can judiciously select materials with right combination of and to get desired temps
  material properties often given as and

## Slide 12: Emissivity & Absorptivity Vary with Wavelength
Designing Space Missions and Systems, Figure 11.29

## Slide 13
Wertz and Larson, SMAD 3rd Edition, Table 11-44
Different editions of SMAD have slightly different tables

## Slide 14: Methods of Thermal Control
Passive Approaches: account for 80%-100% of thermal control of S/C
  surface coatings (focus on and ) (e.g. silver, gold, aluminum)
  MLI (multilayer insulation)
    layers w/low emittance coatings separated by low conductivity layers
  radiators (high emissivity to dump heat overboard S/C)
  heat sinks: high conductivity path away from hot components
  phase change materials
    paraffin absorbs heat as it melts (latent heat of fusion)
    for use next to eqmt w/high, short bursts of power
  heat pipes
    fluid inside sealed tube vaporizes on hot end
    condenses on cool end
    wicking device pulls cool fluid back to hot end
  thermal isolators: isolate propellant lines, etc.
  rotisserie/BBQ roll: slowly rotate S/C (used during Apollo missions)

## Slide 17: Methods of Thermal Control
Active Approaches:
  louvers: insulated blades variably cover radiators (changes effective emissivity)
  electric heaters
  thermoelectric coolers
  expendable cooling systems: stored cryogens absorb heat are then vented to space
  active refrigeration: remove heat from hot components and transport to radiators

## Slide 20: Example of Full TCS Approach

## Slide 21: Thermal Equilibrium
For thermal equilibrium: thermal input = thermal output
(at Earth’s distance from the sun)
Where
= absorptivity (unitless)
= cross-sectional area exposed to heat input (m2)
*Note for an isothermal sphere
= radius of the Earth (km)
= altitude (km)
= emissivity (unitless)

## Slide 22: Worst Case Hot & Cold
Where does worst case hot & cold occur during each orbit?
  Worst-case hot: S/C in direct sun (angle of incidence = 0°)
  Worst-case cold: S/C just about to exit eclipse (longest time in eclipse)

## Slide 23: Calculation Approach
Model S/C and deployed solar arrays separately
Model worst-case hot and worst-case cold
  Model S/C as isothermal sphere, radiating in all directions, receiving heat on a projected side
  Model solar arrays as flat plates
    Front and back of arrays have different emissivity and absorptivity values

## Slide 24: Spacecraft Body (1/3)
Model as isothermal sphere w/ same surface area as actual S/C
Areas, A, for solar, albedo and Earth IR are projected area of a sphere, Ac (1/4 of total sphere surface area)
  where is cross-sectional (projected) area, SA = total surface area of a sphere
Assume uniform power dissipation (from internally generated heat) over entire surface

## Slide 25: Spacecraft Body (2/3)
Worst-case hot:
In , term must account for emitting over entire surface area of S/C (use total SA for area)

## Slide 26: Spacecraft Body (3/3)
Worst-case cold:
In , term must account for emitting over entire surface area of S/C (use total SA for area)

## Slide 27: Deployed Solar Arrays (1/2)
Worst-case hot: assume S/A perpendicular to sun (top face receives direct solar power, bottom face receives albedo and Earth IR)
(some incident power becomes electricity and leaves S/A)
In , term must account for emitting out both front and back faces of the S/A
with

## Slide 28: Deployed Solar Arrays (2/2)
Worst-case cold:

## Slide 29: Example
Given:
  h = 700 km, circular orbit
  Cube-shaped satellite: 2.5 m2 per side
  Internal S/C power: 450-500 W
  Deployed solar arrays are 7 m2
  S/As produce 1350 W at BOL
Find: Hot and cold equilibrium temps for spacecraft body and solar arrays
 | aS | eIR
S/C | 0.6 | 0.8
S/AFront | 0.805 | 0.825
S/ABack | 0.975 | 0.874

## Slide 30: Solution (1/4)
S/C Body
surface area, A = (6)(2.25 m)2 = 30.375 m2
projected area of sphere with same surface area, Ac = A/4 = 7.594 m2
Hot:
oC

## Slide 31: Solution (2/4)
S/C Body
Cold:
oC

## Slide 32: Solution (3/4)
Solar Arrays:
Hot:
oC

## Slide 33: Solution (4/4)
Solar Arrays:
Cold:
oC