## Slide 1
Astro 331 Lesson 27
Assembly, Integration and Test (AI&T)
SMAD Ch 12, Supp Crs Mtl

## Slide 2: Lesson Objectives
Understand common hardware nomenclature
Understand why items are tested at the unit and subassembly level before integration into the vehicle
Describe the differences in intent and application of qualification, protoqualification, and acceptance testing
Understand and describe a flow chart of vehicle-level tests and explain why the tests are conducted in a particular order
Explain the purpose of electromagnetic compatibility, shock, and thermal vacuum testing
Understand the purpose of and differences between spacecraft acoustic tests, sinusoidal sweep vibration tests and random vibration tests
Explain the phrase “test like you fly” and give examples of some test considerations

## Slide 3: *Note
Most of the material from this lesson comes directly from MIL-STD-1540E, Test Requirements for Launch, Upper-Stage, and Space Vehicles
  It would behoove you to read through it…
TYLF info comes from Aerospace Report

## Slide 4: Hardware Nomenclature
Piece part: individual part such as resistor, integrated circuit, bearing, circuit board or housing
Component: complete functional unit such as a control electronics assembly, an antenna, a battery, or a power control unit
Assembly: functional group of parts such as a hinge assembly, an antenna feed, or a deployment boom
Subsystem: all of the components and assemblies that comprise a spacecraft subsystem
Spacecraft: complete vehicle made up of all subsystems and the payload

## Slide 5: Test Levels
Unit Test: testing a component before it is integrated into subsystem, to ensure it works as expected and meets all unit-level requirements
  Note: we expect that suppliers of piece parts test individual piece parts before sending to the contractor to build, so “unit test” refers to tests at the component level
Subsystem Test: testing a subsystem before it is integrated into the vehicle, to ensure all components work together as expected to meet subsystem-level requirements
Vehicle Test: testing all subsystems together, to ensure they all work together as expected across range of requirements

## Slide 6: Test Categories
Functional: demonstrates all functional capabilities expected from an article (unit, subsystem, vehicle); ie, gives expected telemetry, receives expected commands, etc.
Acceptance: demonstrates acceptability of each deliverable item to meet performance specification and demonstrate error-free workmanship in manufacturing
  Lowest test level, required by all flight items
  Meets all requirements over expected ranges (temperatures, stress, etc)
Qualification: demonstrates that the design, manufacturing process and acceptance program produce hardware/software that meet specification requirements with adequate margin
  Highest test level, ensures that units will remain flight-worthy after surviving multiple acceptance tests
  Meets all requirements beyond expected ranges, intended to stress items
  Sometimes performed on test units, rather than flight units
Protoqualification: hybrid of qualification and acceptance testing; applies reduced qualification-level testing to hardware
  Middle test level, would replace qualification
  Uses flight units for testing
  Compromise for qualification testing, when it is not practical/affordable to have a full engineering model to qualification test
  First unit is put through protoqualification test levels, subsequent vehicles are just acceptance tested (sometimes called “qualification by similarity”)

## Slide 7: Unit Level Acceptance
Test is to expected on-orbit levels
Unit is flight-worthy

## Slide 8: Qualification
Qualified item is non-flight
Subsequent flight items are then acceptance tested

## Slide 9: Protoqualification
Protoqualified item is flight
Subsequent flight items are then acceptance tested

## Slide 10: Vehicle Level Test Summary

## Slide 11: Example Integration & Test Flow
Spacecraft Assembly & Integration Complete
Inspection
Full Functional Test
Pressure/Leakage Test
EMC
Acoustic
Vibe
Shock/Deployment
Thermal Balance/TVAC
Pressure/Leakage Test
Pressure/Leakage Test
Full Functional Test
1
2
3
4
5
6
7
8
9
10
11
12
Inspection
13

## Slide 12: Test Types

## Slide 13: Specification Performance (“Full Functional”) Test
Verifies that the mechanical and electrical performance of the vehicle meets requirements, including compatibility with GSE (ground support equipment) and validates all test software and techniques
Demonstrates operation of all redundant units

## Slide 14: Pressure and Leakage Tests
Demonstrate the capability of pressurized subsystems to meet specified flow, pressure and leakage rate requirements

## Slide 15: Electromagnetic Interference & Compatibility (EMI & EMC) Test
Demonstrates electromagnetic compatibility of vehicle to operating environment (launch is bigger concern – both LV and ground communicating w/ LV, on-orbit operations have less interference)
Two major types:
1. Conducted & Radiated Emissions:
    Conducted: consists of electromagnetic interference in circuits that could create issues in delivered power quality due to interference caused by harmonics due to linear and non-linear loads present in the electrical power subsystem and harnessing
    Radiated: comes from antenna when it produces its waveform
2. Conducted & Radiated Susceptibility: ability of a system to operate acceptably when subjected to electromagnetic interference (conducted) and radio frequency voltage or current (radiated)
    Tested by having expected radio frequencies (from LV or ground) radiated at vehicle while performing nominal operations

## Slide 16: Anechoic Chamber
Image Courtesy of
Technische Universitat Wien

## Slide 17: Shock/Deployment Test
Demonstrates the capability of the vehicle to withstand induced shock environments (ie, launch vehicle separation, solar array deployment, etc)

## Slide 18: Solar Array Deployment: Juno & GOES-R
Image Courtesy of
pds-rings.seti.org
Image Courtesy of
pds-rings.seti.org

## Slide 19: Acoustic Test
Demonstrates ability of the vehicle to endure high-frequency (>100 Hz) acoustic environment during launch and ascent
Detects manufacturing and workmanship errors stimulated by higher frequencies

## Slide 20: Acoustic Chamber (Orion Service Module)
Image Courtesy of
spaceflightinsider.com

## Slide 21: Vibration Test
Demonstrates ability of the vehicle to endure the low-to-mid frequency (0-100 Hz) launch environment and verify expected modes and damping
Detects manufacturing and workmanship errors stimulated by low-to-mid frequencies
Two approaches:
  Random: derived to approximate sine vibration of launch vehicle, used with a force-limiting approach to limit loads
  Sinusoidal Sweep: sweeps from low to mid-level frequencies at a levels based on expected interface acceleration levels from modelling
  Typically perform low-level sine sweeps before and after a random to verify no changes in response

## Slide 22: Thermal Tests
Thermal Balance Test
  Provides the data necessary to verify the analytical thermal model and demonstrates the ability of the vehicle TCS to maintain specified temperature limits of all units for various operational scenarios
  Can be combined with TVAC
Thermal Vacuum Test (TVAC)
  Demonstrates ability of vehicle to meet design requirements and establishes thermal design margin and vehicle performance under TVAC conditions and temperature extremes
  Detects material, process and workmanship defects that would respond to thermal vacuum and thermal stress conditions

## Slide 23: Thermal Vacuum Test
Image Courtesy of Huber+Suhner
Image Courtesy of Scientific & Academic Publishing

## Slide 24: Test Like You Fly (TLYF)
Concept of testing a system in the same manner in which it will be used in an operational manner
  Very complicated to implement
  General considerations:
    Flight command & telemetry tested with actual ground software
    Fault condition detection
    Mode/state changes
    Off-nominal condition responses
    Post-environmental test repairs tested
    Flight-like stimuli for responses, appropriate simulators
    Extended test time (DITL, WITL)
    Primary and redundant hardware
    Exercise at high, low, nominal voltages
Consider how to capture data that verifies that test objectives are met