## Slide 1
Astro 331
Structures & Mechanisms
SMAD Ch 11.6

## Slide 2: Lesson Objectives
Explain spacecraft structures and mechanisms functions
Describe the various types of loading conditions that happen during launch and ascent
Identify common characteristics used when selecting materials for spacecraft structures and mechanisms
Analyze monocoque cylinder structures with respect to natural frequency, strength, and buckling
Understand some of the challenges of designing mechanisms for spacecraft

## Slide 3: Structures & Mechanisms Functions
Mechanically support all other S/C subsystems
  Survive all loading conditions
    Not just launch, but also during assembly, test, transport to launch site, as well as operations (deployment of mechanisms, etc)
Attach S/C to L/V
Provide for ordnance-activated separation

## Slide 4: Preliminary Design Process

## Slide 6: Loading Conditions During Launch & Ascent
Resonance: Launch vehicle’s natural frequencies can respond to forces from internal (engine oscillations) and external (aerodynamic effects) sources
    Potential sources of resonance: oscillations in the propulsion system (pogo), aerodynamic buffering during ascent, bending of solid rocket motors
Axial, bending, and torsional modes
Load factors (multiples of weight at sea level): Acceleration from rocket thrust, as well as wind gust and vehicle maneuvers, impart loads
Random vibration: caused by acoustic noise from launch and aerodynamic turbulence during ascent
Pyrotechnic shock: comes from explosive separation events like separation from launch vehicle

## Slide 7: How do we model all of these loading conditions?
Combine math models of the spacecraft and launch vehicle to do what’s called a coupled loads analysis
Drive the coupled model (S/C + L/V) with forcing functions that are based on measured launch vehicle environments

## Slide 8: Materials Selection (1/2)
Material that an object is made out of will determine its response to various loading conditions
Typical S/C has both metallic and nonmetallic materials
  Metals: homogenous (constant properties) and isotropic (same properties regardless of direction of loading)
  Nonmetals: composite materials – not homogenous and often not isotropic

## Slide 9: Materials Selection (2/2)
Materials are selected based on the following properties:
  Strength
  Stiffness
  Density (related to weight)
  Thermal conductivity
  Corrosion resistance
  Cost
  Ductility
  Fracture toughness
  Ease of fabrication
  Versatility of attachment options
  Availability

## Slide 10: Stress and Strain

## Slide 11: Stress/Strain Curve

## Slide 12: Stress/Strain Curve (Explained)
Elastic (linear) region is where a material will return to its original length after a stress
  Until Point A
Beyond a stress called the proportional limit, the material’s stress-strain curve is no longer linear (inelastic)
  Between points A and B
Beyond the proportional limit, the material will undergo residual strain
  Between points B and C
Finally, there is a yield point where a material will rupture (Ultimate Failure)
  Point C

## Slide 14: Cylinder, Skin-Frame, & Truss Structures
Adapted from Designing Space Missions and Systems, Tables 11.45 through 11.48

## Slide 15: Cylindrical Structures
Monocoque cylinder (soda can)
  shell without stiffeners or ring frames
  strength limited by its buckling stress
  difficult to mount components w/o overloading the shell
  may require access panels
Skin-stringer cylinder
  skin designed to buckle at low loads
  stringers carry most of axial load and bending moment
Stiffened-skin cylinder
  thin skin and lightweight
  closely-spaced stiffeners to increase skin’s buckling stress
Semi-monocoque cylinder
  intermediate ring frames to increase skin’s buckling stress
  no axial stiffeners or stringers
  may require access panels
stringers provide hard points for introducing loads

## Slide 16: Sandwich, Isogrid, & Orthogrid Structures
Adapted from Designing Space Missions and Systems, Tables 11.49 & 11.50

## Slide 17: Other Structures (1/2)
Skin-frame structures
  skin surrounding a skeletal framework
  to be stable, ends of skin-stringer structure must be closed with skin, be “triangularized” with diagonal members, or include radially deep frames (as in hexagonal figure)
  sandwich and isogrid panels can be used to mount components
  versatile regarding shape
Truss construction
  withstands loads applied to its joints w/members loaded only axially
  fabrication
    extruded tubes or open shapes
    truss sides integrally machined from plate –stock matl
    laminated composite tubes w/metallic end fittings
  S/C components mounted internally or externally
  can be difficult to transfer loads from truss to cylindrical structure
  most efficient for square, rectangular or triangular cross section structures (less efficient as cross section becomes more round

## Slide 18: Other Structures (2/2)
Sandwich construction
  high in-plane bending stiffness and low mass
  weak in the out-of-plane direction
  often must reinforce sandwich around local areas of attachment (brackets, metal inserts)
  honeycomb core must be vented (small perforations btw cells)
Isogrid and orthogrid
  light-weight plates w/high bending strength and stiffness and shells w/high buckling strength
  peg-board-like grid (at all rib intersection locations) for attachment points
  fabrication
    isogrid with or without skin
    orthogrid always with skin
  isogrid is virtually isotropic but orthogrid is not

## Slide 19: Modeling Monocoque Structures
Look at three loading conditions
  Resonance (natural frequency)
    Goal: want our spacecraft to have a higher natural frequency than launch vehicle
  Strength
    Goal: cylinder must be strong enough to tolerate design load limit factors
  Buckling
    Goal: want the calculated stress due to buckling (stress at which material will buckle) to be greater than the equivalent ultimate stress (expected stress due to loading conditions)

## Slide 20: Natural Frequency (1/2)
(lateral beam)
(axial beam)
Where:
  = natural frequency (Hz)
  E = Young’s modulus (Pa)
  I = area moment of inertia of beam’s cross-section (m4)
  = mass of the beam (uniformly distributed) (kg)
  L = beam length (m)
  A = cross-sectional area of beam (m2)
*Note: The lateral natural frequency tends to be the limiting case (ie, the thickness required to avoid resonance in the axial case tends to be smaller than the thickness required for the lateral case)

## Slide 21: Natural Frequency (2/2)
Where the area moment of inertia can be modelled with:
(box)
(thin-walled cylinder)
And the area of the thin-walled cylinder can be approximated with:
Where:
  b = base of cross-sectional area (m)
  h = height of cross-sectional area (m)
  R = radius of cylinder (m)
  t = thickness of cylinder (m)

## Slide 22: Strength (1/2)
For a cylinder, we can combine axial load (Pax) and the bending moment (M) into an equivalent axial load (Peq)

## Slide 23: Strength (2/2)
To get ultimate design load, we need to apply the factor of safety.
The stress level associated with that load, because stress = force per unit area:
For a cylinder, the area is:

## Slide 24: Buckling (1/2)
Assumes we are in elastic (linear) region of stress-strain curve
  must be less than material’s proportional limit
Where:
  = critical buckling stress (Pa)
  = reduction factor used to correlate theory with test results (unitless)
  E = Young’s modulus (Pa)
  t = thickness (m)
  R = radius (m)

## Slide 25: Buckling (2/2)
Reduction factor
Where:
Conditions for this equation to be valid:
  R/t < 1500
  L/R < 5

## Slide 26: Mechanisms
Mechanism: moving mechanical assembly
Two categories:
  High-cyclic: must move many times during mission
  Low-cyclic: moves only once or a small # of times
Design challenges:
  Thermal expansion/contraction due to changing temperatures on spacecraft
  Inducing vibration to spacecraft
  Friction within mechanism
  Failure due to repeated use
  Harness routing without causing wire damage

## Slide 27: Mechanism Uses
High-cyclic:
  Antenna pointing & tracking
  Solar array pointing & tracking (for sun-tracking arrays)
  Attitude control (reaction wheels or CMGs)
  Switches within TT&C subsystem
Low-cyclic:
  Antenna on-orbit deployment
  Solar array on-orbit deployment
  S/C - L/V separation

## Slide 28: Mass Growth
Designing Space Missions and Systems, Fig 11.38

## Slide 29
0.35 m
Given:
1st lateral fundamental frequency ≥ 35 Hz
Design limit load factors for sizing primary structure
Axial = 6 g’s
Lateral = 1.5 g’s
Ultimate factor of safety FSult = 1.25
Yield factor of safety FSyield = 1.1
Find:
Minimum cylinder thickness to account for natural frequency, strength, and buckling
240 MPa
Yield Stress (σy)
(σu)

## Slide 30: Solution (1/5)
Must consider natural frequency, strength, and buckling
Natural frequency ≥ 35 Hz
assume mass evenly distributed & treat cylinder as a cantilevered beam
solving for I results in
for a thin-walled cylinder
solving for t results in

## Slide 31: Solution (2/5)
Cylinder strength
Cylinder must be strong enough to tolerate design load limit factors
Design Limit Load, :
where 0.75 is assumed to be the height of S/C center of mass from its base (the moment arm)
Design Ultimate Load, :
Peq = limit load, so now apply the factor of safety to get design ultimate load
the stress level associated with that load is
solve for cylinder thickness to tolerate the load and not exceed ultimate strength
in a similar fashion, solve for cylinder thickness to tolerate the load and not exceed yield strength

## Slide 32: Solution (3/5)
Cylinder buckling
can’t solve for thickness directly this time
start w/ largest value for thickness based on strength and stiffness (tmax)
if it satisfies the buckling requirement, no need to go further
if it doesn’t, use iteration to solve for a thickness that will meet buckling
check R/T < 1500 and L/R < 5 to use equations
which is < 1500
which is < 5
so we can continue

## Slide 33: Solution (4/5)
Cylinder buckling (continued)
σeq(ult) is worst case expected stress using max thickness determined so far
<<
so likely less than proportional limit which means we can use our equation
load that will cause buckling (5.68 MPa) < load we expect to see (48.84 MPa) so we are not OK with wall thickness we have
Iterate for t using

## Slide 34: Solution (5/5)
Cylinder buckling (continued)
Iteration Process
You will need to use Excel or Matlab to solve, since there is a “t” variable within the variable for critical buckling stress, but then there is also a “t” variable within the equivalent ultimate stress, so you have to modify them both at the same time.
Thus, the minimum cylinder wall thickness to prevent buckling is

## Slide 35: Answer
Natural Frequency
Strength
  (ultimate strength)
  (yield strength)
Buckling
Most limiting