## Slide 1: Lesson 16
Propulsion, Launch Systems, and Mission Operations

## Slide 2: Propulsion

## Slide 3: S/C Propulsion Functions
Provide for:
  Attitude control
  Momentum dumping
  Orbit maintenance
  Maneuvers

## Slide 6: Ideal Rocket Eqn (and its variants)
Review of basic rocket theory
  Newton’s 3rd Law – equal and opposite reactions
  Newton’s 2nd Law – derive
Where
  = force of thrust (N)
  = linear momentum (kg·m/s)
  = mass (kg)
  = velocity
  = time rate of change of mass (kg/s)
  = acceleration (m/s2)

## Slide 7: Basic Parameters of Rocket Design (1/2)
Thrust
Where
  = force of thrust (N)
  = propellant mass flow rate (kg/s)
  = propellant exhaust velocity (m/s)
  = nozzle exit area (m2)
  = gas pressure at nozzle exit (Pa or N/m2)
  = ambient pressure (Pa or N/m2)

## Slide 8: Basic Parameters of Rocket Design (2/2)
Specific Impulse
  Ratio of the thrust to the weight flow rate of the propellant – it is a measure of the efficiency of the flow (a larger number is better)
Where:
  = force of thrust (N)
  = mass flow rate (kg/s)
  = acceleration due to gravity of central body (m/s2) (9.807 m/s2 for Earth)

## Slide 9: Ideal Rocket Equation
Developed by Konstantin Tsiolkovsky in 1903:
Where:
  = velocity change produced by propulsion system (m/s)
  = specific impulse (s)
  = acceleration due to gravity of central body (m/s2) (9.807 m/s2 for Earth)
  = initial vehicle mass (kg)
  = final vehicle mass (kg) (after propellant has been expended)

## Slide 10: Classic Rocket Engine
Note that we achieve greatest thrust when exit pressure = ambient pressure
  Although it looks like thrust would be greater with exit pressure greater than ambient pressure, the exhaust velocity is reduced, resulting in a loss of thrust
  Thus, we design rocket exhaust nozzles with an exit pressure equal to ambient pressure whenever possible

## Slide 12: Nozzle Expansion
Patmos > Pexit
Patmos = Pexit
Patmos < Pexit

## Slide 13: Nozzle Expansion
For spacecraft propulsion, where the ambient pressure is zero, thrust is always higher with larger nozzle expansion ratios:
Where
  = nozzle area expansion ratio (unitless)
  = area of nozzle exit (m2)
  = area of the throat (m2)

## Slide 14: Common Types of Spacecraft Propulsion (1/2)
Cold gas
  Controlled, pressurized gas source with a nozzle
    Simplest form of a rocket engine
Chemical
  Liquid: stored as liquids in tanks and fed on demand into the combustion chamber by gas pressurization or a pump
    Bipropellant: chemically react a fuel and an oxidizer
      Higher specific impulse but additional complexity and cost
    Monopropellant: catalytically decompose a single propellant
  Solid: stores propellants in solid form
    lower specific impulse, but simpler than liquid engines
  Hybrid: propellants are stored in different forms; typically, fuel is solid and oxidizer is a liquid or gas
    Attractive because of safety, allow for throttling and restart, fuel storability, environmentally clean

## Slide 15: Liquid Bipropellant

## Slide 16: Liquid Monopropellant

## Slide 17: Solid

## Slide 18: Hybrid

## Slide 19: Common Types of Spacecraft Propellant (2/2)
Electric: produces thrust using externally provided electrical power either from Sun, nuclear, or thermodynamic conversion to accelerate fluid.
  Electrothermal: gas heat via resistance element or arc and expanded through nozzle
  Electrostatic: ions electrostatically accelerated
  Electromagnetic: plasma accelerated via interaction of current and magnetic field

## Slide 20
Electric Propulsion Comparison

## Slide 21: Advanced Propulsion Concepts (gee-whiz)
Solar Sails – large sheets of thin reflective material, using photons to push the sail
Solar Thermal – use large solar reflectors to heat propellant in a “combustion” chamber
Nuclear Thermal – heat propellant in “combustion” chamber using a nuclear reactor

## Slide 22: Performance Comparison of Different Propellants
Technology | Isp (sec) | Thrust (N)
Chemical | 140 – 450 | 0.1 – 12,000,000
Electric | 1000 – 10,000 | 0.0001 - 20
Nuclear | 800 – 1100 | Up to 12,000,000
Cold Gas | 60 - 250 | 0.1 - 50

## Slide 23
Advantages & Disadvantages
 | Pros | Cons
Chemical - Liquid | Higher Isp Throttleable Re-start able | Two propellants - complicated Intense combustion temps Sometimes cryogenic Sometimes toxic
Chemical - Solid | Simple Reliable No propellant management Higher Thrust-to-Weight | Cracks can form in propellant grain No restart Can’t stop Modest Isp
Electric | Simple Can achieve very high specific impulses No moving parts | Large amount of electrical power Low thrust
Nuclear | Long-term energy supply High Isp High thrust | Environmental issues Political issues No flight heritage
Cold Gas | Simplest Safest Restart able Throttleable | Low Isp

## Slide 24: Propulsion Systems Suitability

## Slide 25: Propellant Tank Sizing (1/3)
Calculate propellant volume using densities
  (Table 17-4)
Add additional volume to account for ullage & possible shrinkage (an issue for cryogenic fuels)
  Ullage: extra tank volume at the top of the tank to provide space for pressurization gas

## Slide 27: Calculate Tank Size (2/3)
(3) Select general tank geometry: solve for dimensions and mass
 | Tank Shape |  | 
 | Spherical | Cylinder with Hemispherical Caps | Reference
Volume |  |  | Std definition
Surface Area |  |  | Std definition
Wall Thickness |  |  | 
 | Tank Shape |  | 
 | Spherical | Cylinder with Hemispherical Caps | Reference
Volume |  |  | Std definition
Surface Area |  |  | Std definition
Wall Thickness |  |  | 

## Slide 28: Calculate Tank Size (3/3)
= propellant volume (m3)
= surface area of tank (m2)
= radius of tank (m)
= cylinder length of tank (m)
= tank operating pressure (Pa)
  Assume ~20.7 MPa for high-pressure (gas) tanks
  Assume ~2.07 MPa for low-pressure (liquid) tanks
= tank thickness (m)
= limit stress of tank material
= material density (kg/m3)
[note: chart gives values in g/cm3  multiply by 1000 to get kg/m3]

## Slide 29: LAUNCH SYSTEMS

## Slide 30: Launch Systems
Purpose: to accelerate and position spacecraft up to the velocity and location required for the payload’s desired trajectory
Staging: using multiple propulsive units which separate and are discarded after use to get to orbit
  Why do we do staging?
    B/c of the performance limitations on chemical propellants as well as the current state of the art in materials engineering and structural design, it is not practical to send a launch vehicle to orbit using a single propulsion system.

## Slide 32: Payload Fairing (PLF)
Protects the payload from aerodynamic and heating loads as the LV climbs out of the atmosphere, keeps FOD away from payload, and serves as a container with a specially conditioned atmosphere to meet the payload’s thermal requirements
  PLF is jettisoned once environment is safe for payload (above atmosphere)
  Shock associated with the PLF jettison can be among the most significant transient design environment that a spacecraft must endure

## Slide 35: Maximum Dynamic Pressure
Max-Q (maximum dynamic pressure): point during ascent at which aerodynamic loads on vehicle are at highest
  Sets maximum bending load values for vehicle (and payload)
  Usually occurs just after vehicle passes Mach 1
  Buffeting loads are also highest near Max-Q
  Common for motors to be throttled back near Max-Q to reduce vehicle acceleration and loading
  After Max-Q, the atmospheric density decreases faster than the vehicle’s speed increases, which causes the dynamic pressure to decrease

## Slide 37: Loading Conditions during Launch & Ascent
Axial and lateral loading during liftoff
Vibrations during liftoff
Acoustic loading due to noise during liftoff & ascent
Pyrotechnic shock due to separation events

## Slide 44: Launch Limitations
Recall that the latitude of the launch site must be less than or equal to the inclination of the orbit
Recall also that each launch site has allowable launch azimuths that must be met
Also need to consider transportation of spacecraft to launch site and weather at launch site during expected launch timeframe

## Slide 50: MISSION OPERATIONS

## Slide 51: Space Mission Operations
Execute the mission and preserve the health and safety of the vehicle
Functions include:
  Mission Planning: deciding what to do and when
  Activity Planning & Development: creating operational scenarios and developing command loads
  Mission Control: managing daily activities
  Data Transport and Delivery: establishing communication links and managing data flow
  Navigation and Orbit Control: determining where the spacecraft is and planning maneuvers
  Spacecraft Ops: managing the spacecraft bus
  Payload Ops: managing the spacecraft payload

## Slide 53: Mission Planning
Operations Plan: details the operations organization, processes and procedures to be followed by the operations team, the software tools that support them, and the interfaces between other teams (ie, spacecraft development team)
  Best way to train operators it to involve them in the development and testing phases
Mission Plan: documents the planned spacecraft activities during the mission

## Slide 54: Extra Material

## Slide 55: Automation in Operations (1/2)
Many functions in space operations can be automated, either on-board the spacecraft or on the ground.
  Monitoring alarms
  Managing spacecraft resources
  Analyzing performance and trends
  Onboard navigation & orbit control
  Adaptively planning activities
  Processing payload data
  Detecting faults, safing the vehicle
  Constraint checking commands
  Filtering/archiving data

## Slide 56: Automation in Operations (2/2)
Advantages | Disadvantages
Reduced staffing = reduced operations cost | Potential to miss unexpected signatures
Reduced changes for operator error | Potential for fault response to be improper
Reduced response time to fault responses | Potential to misuse spacecraft resources
Potential to reduce data transmitted from spacecraft to ground | Potential to damage spacecraft
*Decision on how much and where to automate depends on risk posture, mission objectives and budget

## Slide 57: Contingency Planning (1/2)
Identifying potential problems and a plan of action to mitigate impact if problem occurs
  Not every problem can be anticipated, but the process of developing a contingency plan helps prepare the team to deal with problems when they occur
  Prior to flight, identify anomaly response team – should have members of operations and development teams (and possibly other teams)
  Prior to flight, the design and operations teams should work together to brainstorm every conceivable potential anomaly and for each case, develop operational responses
  During flight, have development team members support operations

## Slide 58: Contingency Planning (2/2)
In case of a failure:
  Determine how much time is available before a decision is required
  Make a timeline of events and include everything that is known
  Give all team members all known facts and check every theory against them
  Have multiple teams: some should investigate timeline replanning, others should work on hardware/software repair or workarounds
  Make sure any deviation from the norm is explained—remember, the wrong conclusion is prologue to the next failure
  Do not arrive at a conclusion too rapidly
  Know when to stop trying to force-fit a scenario