## Slide 1
On Board Computing
Lt Col Miller
Notes: Quickbird

## Slide 2: Commanding
Telemetry
C&DHS

## Slide 3: TT&C
Telemetry - The in situ collection of measurements or other data at remote points and their automatic transmission to receiving equipment for monitoring.
  Telecommand
  Tracking
  Status of Health

## Slide 4: CD&H
Command Data and Handling
  Telecommand
  Data handling
Components
  On board Computer
  Radio
  Ground Station Equipment
    Wire Harnesses
    Protocols
    Modulation
    Data Frames

## Slide 5: Comm Path
S/C to ground
  ADC
  Multiplexing – combining multiple signals
  Modulation – putting info onto EM wave
  Amplification
Ground to S/C
  Amplification
  Demodulation
  Demultiplexing
  DAC

## Slide 7: For 331
Computer
  On board computing
  Faults
  Reliability
Radio – Comm lesson from before
Both COTS materials

## Slide 10: On Board Computer
Flight Computer
  FlatSat – Arduino
  Apollo – Bespoke 15 (16 bit computer)
  DMSP – 32 K of memory
  Space Shuttle – Intel 8086 (1MB of memory)
  ISS – Intel i386 (state of the art for 1985)
  Dragon – Linux based dual core x86 (2012)
    C++, Python, HTML

## Slide 11: What could go wrong?
software bugs
electrical design flaws
radiation effects
pre-launch corrosion
thermal-electrical stress
thermal-mechanical stress
mechanical stress during launch
manufacturing and assembly errors

## Slide 12: Radiation Effects
single event effects
  single event transient (SET) spurious signal
  single event upset (SEU) state change (memory, storage, etc.)
  single event latchup (SEL) switch closes and stays closed until a power cycle
    bad if it shorts power to ground

## Slide 13: Radiation Effects
total ionizing dose effects
  cumulative radiation exposure
    COTS tolerance: 1–10 krad
    rad hard tolerance: 0.1–1 Mrad

## Slide 15: Faults
Fault: an unexpected response whereby the function is recoverable, either by fixing it, managing around it, or by redundancy
Fault tolerance: the number of faults that the system must tolerate to meet its specifications
Fault mitigation: the passive mitigation of faults through design
  Examples: ARM/EXECUTE command pairs for hazardous commands, extra solar array strings

## Slide 16: Faults
Fault protection: the implementation of design intended to actively control the effects of a fault
  Limited to detecting and responding to discrete defects which may arise in the operation of an otherwise healthy space vehicle
  Intended to detect faults (or the effect of a fault) and intervene so that the fault does not permanently affect the safety of the space vehicle
Safe Hold Mode

## Slide 17: Faults
Fault management: an engineering discipline that addresses the occurrence of faults on the space vehicle and provides a means for reducing their effect through cooperative design of both the space vehicle and ground elements and operator actions; includes fault tolerance, fault mitigation and fault protection

## Slide 20: Non-Computer Failures
Part Screening – screen out part that are likely to fail in service

## Slide 21: Non-Computer Failures
Process Control– screening the process of manufacturing the part

## Slide 22: Reliability over Time

## Slide 23: How to deal with Failures
Testing to prevent
Redundancy
Graceful Degradation

## Slide 24: Reliability